## Slide 1: YAPT Provision SRX devices
Christian Klewar (cklewar@juniper.net)
Version 0.2 / Feb 2017
Quick Start Guide (Virtualbox)

## Slide 2: YAPT- Prerequisites
To use this quick start guide we need vagrant and VirtualBox being installed. This Quick Start uses staging area approach with OSSH plugin. There are more options which could be used like: PHS / TFTP / DHCP
➜ ~ vagrant -v
Vagrant 1.8.6

## Slide 3: YAPT - Vagrant Box Topology
vSRX
YAPT Server
(WebUI)
VirtualBox
YAPT Server
(DHCP / OSSH)
Private Network: vboxnetX 172.28.128.0/24
Download YAPT Vagrant file from: https://git.juniper.net/cklewar/YAPT/tree/dev/vagrant
Unzip Vagrant box file
  tar xvfz yapt-vagrant.tar.gz
Bring VM up
  cd yapt-vagrant
  vagrant up
Download vSRX image
Convert image from vmdk to vdi
Configure vSRX VM settings
  Download vSRX (15.1X49-D1xy) image
  Edit vSRX Network settings
  Set Adapter1
    Attached to: internal-network
    Name: yapt-staging
  Mount juniper.iso image in cdrom
  Start vSRX VM
Connect to YAPT VM
  vagrant ssh
Connect to YAPT WebUI: http://172.28.128.3:8080/yapt/ui
New device will show up after a while in job table
Internal Network: yapt-staging
10.21.41.0/24
Web UI: http://172.28.128.3:8080/yapt/ui
172.28.128.3
10.21.41.2

## Slide 4: YAPT – Start Vagrant (VirtualBox) VM
➜ yapt vagrant up
Bringing machine 'yapt01' up with 'virtualbox' provider...
==> yapt01: Importing base box 'yapt-centos7-01'...
==> yapt01: Matching MAC address for NAT networking...
==> yapt01: Setting the name of the VM: yapt_yapt01_1495015520894_92961
==> yapt01: Clearing any previously set network interfaces...
==> yapt01: Preparing network interfaces based on configuration...
yapt01: Adapter 1: nat
yapt01: Adapter 2: intnet
yapt01: Adapter 3: hostonly
==> yapt01: Forwarding ports...
yapt01: 22 (guest) => 2222 (host) (adapter 1)
==> yapt01: Running 'pre-boot' VM customizations...
==> yapt01: Booting VM...
==> yapt01: Waiting for machine to boot. This may take a few minutes...
yapt01: SSH address: 127.0.0.1:2222
yapt01: SSH username: vagrant
yapt01: SSH auth method: private key
yapt01: Warning: Remote connection disconnect. Retrying...
yapt01: Warning: Remote connection disconnect. Retrying...
yapt01:
yapt01: Vagrant insecure key detected. Vagrant will automatically replace
yapt01: this with a newly generated keypair for better security.
yapt01:
yapt01: Inserting generated public key within guest...
yapt01: Removing insecure key from the guest if it's present...
yapt01: Key inserted! Disconnecting and reconnecting using new SSH key...
==> yapt01: Machine booted and ready!
[yapt01] GuestAdditions 5.1.21 running --- OK.
==> yapt01: Checking for guest additions in VM...
==> yapt01: Setting hostname...
==> yapt01: Configuring and enabling network interfaces...
==> yapt01: Mounting shared folders...
yapt01: /vagrant => /yapt-vagrant/yapt

## Slide 5: YAPT- vSRX
Download vSRX image
Unpack vSRX image
  tar xvf media-srx-vsrx-vmdisk-15.1X49-D110.4.ide.ova
Convert vSRX Image to vdi
  vboxmanage clonehd -format VDI media-srx-vsrx-vmdisk-15.1X49-D110.4-disk1.vmdk junos-vsrx-15.1X49-D110.4.vdi

## Slide 6: YAPT – Configure vSRX Settings

## Slide 7: YAPT – Configure vSRX Network Settings

## Slide 8: YAPT – vSRX Virtualbox Caveats
Running vSRX in Virtualbox only supports fxp0 interface
Control Plane performance is slow since missing nested virtualization support in Virtualbox

## Slide 9: YAPT – SSH into VM / show logs
➜ yapt vagrant ssh
Last login: Fri Apr 28 23:48:51 2017
[vagrant@yapt01 ~]$ sudo su
[root@yapt01 vagrant]# cd
[root@yapt01 ~]# cd junpiper-yapt-0.0.2
[root@yapt01 ~]# tail –f ./logs/info.log

## Slide 10: YAPT– Open Web UI
http://172.28.128.3:8080/yapt/ui

## Slide 11: YAPT – Restart Provisioning Process
vsrx01>request system reboot